## Slide 1
PROCESS DECK
Quá trình thực hiện nghiên cứu Neural Operator VBTS theo phase
Differentiable Neural-Operator Surrogate for Vision-Based Tactile Sensing and Control
FINAL GT
2520
corrected-BC frames
MAIN MODEL
LR-FNO
field-to-field
ACCURACY
0.0606
rel-L2 test
SPEEDUP
29,182x
vs single IPC solve
Neural-operator surrogate for VBTS | phase process deck
01

## Slide 2
map
Roadmap theo phase
Luồng nghiên cứu: chọn ground truth -> học operator -> downstream -> audit vật lý -> mở rộng hình học
Neural-operator surrogate for VBTS | phase process deck
02
Phase | Mục tiêu | Việc làm | Đầu ra
P0 | Khảo sát khả thi | scale gel, mesh, eps, marker sampling | chọn cấu hình chạy production
P1 | Sinh ground truth | IPC/UIPC corrected-BC, K<=5 | dataset 2520 frame
P2 | LR-FNO | operator field-to-field | model chính
P3 | Benchmark | RQ1-RQ3, baselines, multiseed | headline accuracy/speed
P4 | Control | autograd vs ES | sample efficiency
P5 | Sensor | marker renderer + image inverse | render o LR-FNO
P6 | Env | one-step tactile environment | gradient end-to-end
P7 | BC audit | rigid-shift root cause | reground corrected-BC
P8 | Geometry-OOD | zero/few-shot 6 shapes | scope + mitigation

## Slide 3
P0
Phase 0
Khảo sát realistic geometry và ổn định số trước production
04

## Slide 4
P0
Phase 0: Chọn cấu hình mô phỏng
Từ gel lớn/solver cũ sang thin-gel realistic và marker sampling ổn định
Neural-operator surrogate for VBTS | phase process deck
04
Thiết kế vật lý
Gel representative: 20 x 20 x 3 mm.
Marker grid 32 x 32 trên top surface.
Structured tetra mesh; production chọn res24.
Solver knobs
eps_velocity = 2.5e-5.
d_hat = 1e-4; contact resistance = 1e9.
velocity_tol tightened để giảm stochasticity.
Sampling
Nearest-neighbor top markers gây nhiễu theo mesh.
Chuyển sang bilinear marker sampling.
Provenance lưu vào NPZ để trace downstream.
Gate | Kết quả | Quyết định
res20 -> res24 | ~12% drift | res20 quá coarse
res24 -> res28 | tangential 0.95%, normal 1.18% | res24 đạt plateau
K=3 smoke | tangential noise ~1-2% | đủ launch sweep

## Slide 5
P0
Phase 0: Eps-axis và smoke
Bằng chứng chọn eps_velocity nhỏ hơn cấu hình ban đầu
Neural-operator surrogate for VBTS | phase process deck
05
Eps step | Tangential change | Ý nghĩa
0.001 -> 0.0005 | 29.21% | quá thô
0.0005 -> 0.00025 | 19.14% | chưa ổn
0.00025 -> 0.0001 | 10.27% | còn drift
0.0001 -> 0.00005 | 4.97% | gần hội tụ
0.00005 -> 0.000025 | 1.54% | chọn production
Smoke production-shaped
Một frame random realistic: depth 0.614 mm, partial-slip.
K=3 replicate noise: tangential 1.02%, normal 0.10%.
Mean single solve ~11.8 s; K=3 target ~35.4 s.
Kết luận: đủ ổn để chạy production, không overwrite GT cũ.
Artifact chính
data/uipc/conv_realistic_eps_axis_vtol001/convergence_report.json; data/uipc/realistic_phase0/chosen_eps_regimes; infra/gen_uipc_sweep.sh

## Slide 6
P1
Phase 1
Sinh IPC/UIPC ground truth realistic và corrected-BC
07

## Slide 7
P1
Phase 1: Production ground truth
Final dataset dùng cho paper và toàn bộ downstream
Neural-operator surrogate for VBTS | phase process deck
07
FRAMES
2520
2120 train / 400 test
RAW SOLVES
12,600
63 x 40 x K=5
MESH
res24
3125 verts, 13824 tets
MARKER GRID
32 x 32
bilinear sampling
BC
fixed
bottom
Mode | All frames | Test frames
normal | 425 | 68
stick | 712 | 113
partial-slip | 895 | 142
full-slip | 488 | 77
Dataset source of truth
data/uipc/shear_res24_avg_swept_REALISTIC_BC.npz
Provenance: gel_res, eps_velocity, velocity_tol, marker_sampling, solve_time_s.
Downstream JSON đều trỏ về gt_path này.

## Slide 8
P1
Phase 1: Robust averaging
UIPC không bitwise-repeatable, nên target được lọc theo replicate distance
Neural-operator surrogate for VBTS | phase process deck
08
Kept K | Frames | Ghi chú
5 | 1397 | ổn định nhất
4 | 318 | lọc 1 outlier
3 | 331 | noise trung bình
2 | 474 | thường ở full-slip khó
FULL-SLIP UNIFORM
22.0%
mean energy
P95 UNIFORM
27.0%
old soft-BC ~99.8%
Mode | Tangential rep-noise
normal | 1.4%
stick | 2.0%
partial | 3.5%
full | 4.4%
Ý nghĩa
Phase 1 biến solver stochastic thành target đủ sạch cho operator learning, đồng thời giữ disclosure noise trong Limitations.

## Slide 9
P2
Phase 2
Xây LR-FNO field-to-field surrogate
10

## Slide 10
P2
Phase 2: Neural Operator là gì?
Học ánh xạ giữa các trường/hàm, không chỉ hồi quy từng điểm riêng lẻ
Neural-operator surrogate for VBTS | phase process deck
10
input field a(x)
->
Neural Operator
Gθ: a → u
->
output field u(x)
Train offline
IPC/UIPC pairs
->
Infer online
ms latency
Khác MLP local
MLP dự đoán từng điểm dễ bỏ mất ngữ cảnh toàn cục.
Neural operator học toàn bộ trường → toàn bộ trường.
Vì sao hợp với VBTS
Gel bonded có đáp ứng đàn hồi non-local.
Một contact cục bộ làm dịch chuyển cả lân cận.
Vai trò trong nghiên cứu
Amortize solver cost: FEM/IPC sinh data offline.
Surrogate frozen dùng cho control/sensor/env.

## Slide 11
P2
Phase 2: Kiến trúc FNO trunk
Fourier Neural Operator dùng spectral convolution để học kernel toàn cục
Neural-operator surrogate for VBTS | phase process deck
11
Input
a(x): contact channels
->
Lift
1x1 conv / MLP to latent width
->
FFT
spatial field → Fourier modes
->
Low modes
keep k modes learn R_theta
->
IFFT + W
global spectral + pointwise path
->
Activation
GELU / stack L layers
->
Project
u_x,u_y,u_z marker field
FNO layer: v'(x) = σ( F⁻¹( Rθ · F(v) ) + Wv )
Rθ học global kernel trong miền tần số; W giữ biến đổi local/pointwise.
Điểm mạnh
Receptive field toàn cục ngay trong mỗi spectral layer.
Rất hợp với response non-local của gel.
Điểm yếu
Low modes làm trơn chi tiết near-contact.
Cần refinement để bắt biên/sắc thái cục bộ.
Trong deck
FNO trunk là ablation và nền cho LR-FNO.

## Slide 12
P2
Phase 2: Kiến trúc LR-FNO đề xuất
Locally Refined FNO = global spectral trunk + local refinement path
Neural-operator surrogate for VBTS | phase process deck
12
Input field
depth + shear + params
->
Global path
FNO spectral trunk captures non-local response
Local path
2-layer conv stem keeps near-contact features
->
->
Fuse
concat trunk + local + raw input
->
Refinement head
small conv head corrects local residual
->
Output
u_x,u_y,u_z
Component | Vai trò
FNO trunk | global / non-local elastic response
Local stem | near-contact texture and sharp gradients
Refinement head | residual correction with small parameter cost
Evidence | Kết quả
5-seed rel-L2 | 0.0590 +/- 0.0014
vs FNO trunk | wins 5/5 seeds, t=4.72
Cost | +3.3% params, lower fps

## Slide 13
P2
Phase 2: Field-to-field framing
Bài toán được đặt là học toán tử contact field -> marker displacement field
Neural-operator surrogate for VBTS | phase process deck
13
Contact field
->
FNO spectral trunk
->
Local refinement
->
Marker displacement
Input
Indentation profile.
Tangential-drive channel masked to contact.
Physical params R, mu, E.
Why FNO
Gel response is non-local.
Spectral kernel sees global context.
Per-point local MLP collapses on slip.
Why LR
Local stem captures near-contact sharpness.
Small refinement head.
Chosen by multiseed stability.

## Slide 14
P2
Phase 2: Model selection
LR-FNO được chọn bằng five-seed benchmark, không chỉ seed-0 peak
Neural-operator surrogate for VBTS | phase process deck
14
Model | rel-L2 mean/std | dir deg | fps | paired t vs FNO
U-Net | 0.0890 +/- 0.0067 | 2.38 | 19422 | -2.16
FNO trunk | 0.0780 +/- 0.0081 | 1.83 | 7996 | ---
U-FNO-style | 0.0634 +/- 0.0113 | 1.63 | 4784 | +1.85
LR-FNO | 0.0590 +/- 0.0014 | 1.50 | 5676 | +4.72
Quyết định
LR-FNO thắng FNO 5/5 seed, paired t=4.72, std nhỏ.
U-FNO-style có seed tốt nhưng variance lớn; U-Net nhanh nhưng kém chính xác hơn.
Framing khoa học
Gọi là locally refined FNO / U-FNO family adaptation.
Không claim kiến trúc hoàn toàn mới.

## Slide 15
P3
Phase 3
Benchmark RQ1-RQ3: fidelity, generalization, speed
16

## Slide 16
P3
Phase 3: Headline metrics
Số chính từ runs/phase3_fem/benchmark.json
Neural-operator surrogate for VBTS | phase process deck
16
REL-L2
0.0606
LR-FNO overall
DIRECTION
1.42 deg
tangential
MLP GAP
9.0x
field-to-field wins
FPS
5603
operator inference
SPEEDUP
29,182x
single solve
Mode | LR-FNO rel-L2 | MLP rel-L2
normal | 0.046 | 0.366
stick | 0.052 | 0.471
partial | 0.061 | 0.615
full | 0.086 | 0.683

## Slide 17
P3
Phase 3: Baseline bake-off
Bảng native PowerPoint, số từ vbts_baselines.json
Neural-operator surrogate for VBTS | phase process deck
17
Method | rel-L2 | dir deg | FNO adv.
TACTO-style | 0.656 | 69.6 | 8.85x
Cattaneo-Mindlin | 0.830 | 75.2 | 11.19x
Taxim/FOTS linear | 0.302 | 9.3 | 4.07x
MLP per-point | 0.545 | 41.9 | 7.35x
DeepONet | 0.115 | 3.2 | 1.55x
U-Net | 0.085 | 2.2 | 1.15x
Galerkin | 0.151 | 4.1 | 2.04x
FNO trunk | 0.074 | 1.6 | ---
LR-FNO | 0.060 | 1.5 | ---
Kết luận
Classical/analytic/linear marker cores kém rõ trên cùng GT.
Dense neural models tiến gần hơn; U-Net là đối thủ sát.
Thông điệp đúng: field-to-field non-local operator learning là chìa khóa.
Sắc thái
Không claim raw fps thắng mọi simulator.
Lợi thế bền là latency thấp + autograd + mesh-free deployment.

## Slide 18
P3
Phase 3: RQ2 và slip heads
Generalization theo tham số vật lý và phân loại contact mode
Neural-operator surrogate for VBTS | phase process deck
18
OOD axis | Degradation | N OOD
high radius R | 2.10x | 480
high friction mu | 1.63x | 480
high stiffness E | 1.32x | 480
Slip head A | F1
macro | 0.931
binary slip | 0.969
normal | 0.977
full slip | 0.919
Interpretation
Radius là trục nhạy nhất; E bền hơn trong displacement-control. Slip-head tốt nhưng vẫn báo rõ per-class thay vì chỉ macro.

## Slide 19
P4
Phase 4
Học policy điều khiển qua surrogate khả vi
20

## Slide 20
P4
Phase 4: Task design
Servo policy một bước, không phải RL đa bước
Neural-operator surrogate for VBTS | phase process deck
20
Input
Context: mu, E, R, geometry.
Target summary từ tactile field.
PolicyMLP xuất action sx, sy.
Autograd branch
LR-FNO frozen: eval + requires_grad False.
Gradient chỉ đi tới action/policy.
1 backward per step.
ES baseline
OpenAI-ES antithetic.
Same PolicyMLP and optimizer.
Cô lập nguồn gradient.
Scope
Trong simulation, static one-step map.
Dùng để test differentiability/sample-efficiency, không claim closed-loop dynamics.

## Slide 21
P4
Phase 4: Autograd vs ES
Số từ runs/phase4/policy_servo.json
Neural-operator surrogate for VBTS | phase process deck
21
Method | Final loss | Fwd queries | Wall time | Target query
Autograd | 1.94e-10 | 300 | 18.2s | 81
ES pop32 | 2.19e-10 | 19200 | 438.0s | 5824
QUERY
72x
fewer to target
WALL
24x
faster
Finding
Suh-style gradient pathology không xuất hiện ở one-step learned surrogate.
Smooth operator gradient có ích cho control, dù không thay thế multi-step contact proof.

## Slide 22
P5
Phase 5
Cảm biến marker-dot khả vi và image-space inverse
23

## Slide 23
P5
Phase 5: Renderer pipeline
Từ displacement field sang ảnh marker-dot bằng torch
Neural-operator surrogate for VBTS | phase process deck
23
Renderer
Pinhole camera nhìn từ dưới gel.
Deformed markers -> Gaussian dot splatting.
Torch implementation: autograd-connected.
FEM/IPC field
->
marker positions
->
rendered dots
->
image loss
->
gradient

## Slide 24
P5
Phase 5: Sensor metrics
Số từ sensor_build / sensor_compat / sensor_inverse
Neural-operator surrogate for VBTS | phase process deck
24
Metric | Value | Note
flow-disp cosine | 0.999 | mean over modes
round-trip overall | 0.22 px | render -> track
stick / slip px | 0.13 / 0.30 | mode split
compat flow rel-L2 | 0.078 | render o LR-FNO
single inverse | 9.0% / 2.82 deg | full slip
Mode | Mag err | Dir err
normal | 23.3% | 16.9 deg
stick | 5.0% | 1.1 deg
partial | 3.8% | 0.9 deg
full | 15.3% | 0.4 deg
overall | 11.8% | 4.8 deg
Interpretation
Image inverse tốt ở shear-rich regimes; normal khó vì shear gần 0 khiến hướng ill-defined. Report phải tách theo mode.

## Slide 25
P5
Phase 5: Visual evidence
Ảnh lấy trực tiếp từ runs/phase5
Neural-operator surrogate for VBTS | phase process deck
25
Read
GT/FNO residual.
Flow residual.
Mode samples.

## Slide 26
P6
Phase 6
Framework mô phỏng VBTS và differentiable environment
27

## Slide 27
P6
Phase 6: Env wrapper
Frozen LR-FNO + marker sensor + image reward
Neural-operator surrogate for VBTS | phase process deck
27
REWARD GAP
99.8%
random -> oracle
GRADCHECK
5.0%
finite diff
FLOWS TO ACTION
PASS
autograd path
OBS IMAGE
64 px
noisy reward
Scope
Contextual one-step environment, not multi-step dynamics.
Useful proof: policy can optimize through image reward.
Current formal evidence is gradient-flow sanity check.

## Slide 28
P6
Phase 6: 6b-6d framework notes
Các hướng framework còn lại hiện là log/report evidence, không còn đủ artifact trong runs/phase6
Neural-operator surrogate for VBTS | phase process deck
28
Subphase | Finding | Evidence / caveat
6b realism | camera noise floor không che được FNO error | số từ log gốc; cần archive artifact nếu muốn reproducible
6c temporal | endpoint-only đủ; loading-history NULL | model-free kNN matched: cross/same ~1.00
6d object geometry | sphere << cylinder < flat về marker-flow | đặt nền cho Phase 8 geometry-OOD
6a env | artifact còn đầy đủ | runs/phase6/env_demo.{json,png}
Audit note
Báo cáo Phase 6 đã ghi rõ chỉ 6a còn artifact trong runs; khi trình bày chính thức nên phân biệt measured artifact vs archived/log-derived evidence.

## Slide 29
P7
Phase 7
Temporal visualization và audit boundary condition
30

## Slide 30
P7
Phase 7: Soft-BC symptom
FNO khớp GT soft-BC, nhưng GT có rigid drift artifact
Neural-operator surrogate for VBTS | phase process deck
30
Temporal compare | Value
mean rel-L2 | 0.038
EPE | 0.12 px
dir error | 1.17 deg
cos | 0.9997
Interpretation
Soft-BC run chứng minh model khớp lineage cũ, nhưng không phải evidence vật lý cuối vì bottom constraint tạo rigid shift.

## Slide 31
P7
Phase 7: Corrected-BC root cause
Fixed bottom loại bỏ near-rigid tangential drift
Neural-operator surrogate for VBTS | phase process deck
31
Field diagnostic | Soft-BC | Corrected-BC
local normal contrast | 0.085 mm | 0.258-0.262 mm
residual tangential | 0.012 mm | 0.076-0.090 mm
mean marker flow | 3.1-3.3 px | 0.54-0.67 px
uniform energy | ~99.8% | 20-24% smoke

## Slide 32
P7
Phase 7: Evidence hygiene
Không dùng corrected-BC GT-vs-FNO cũ làm claim model
Neural-operator surrogate for VBTS | phase process deck
32
Artifact | Status | Use
runs/phase7/* | soft-BC | temporal visualization only
runs/phase7_bc_corrected/temporal* | corrected GT | GT-only evidence valid
runs/phase7_bc_corrected/temporal_gt_vs_fno | FNO trained on old GT | do not use as FNO evidence
production REALISTIC_BC | rerun complete | source for Phase 3-6
BAD COMPARE
3.37
rel-L2
BAD EPE
2.77px
old model vs new BC
Outcome
Boundary-condition audit triggered full production reground.
All final downstream metrics use corrected-BC dataset.

## Slide 33
P8
Phase 8
Geometry-OOD: đo zero-shot drop và few-shot recovery
34

## Slide 34
P8
Phase 8: Protocol
LR-FNO train trên sphere, test trên 6 hình lệch dần khỏi sphere
Neural-operator surrogate for VBTS | phase process deck
34
IN-DIST REL-L2
0.0588
+/- 0.0016
TANGENTIAL RMSE
3.67um
+/- 0.14
OOD SHAPES
6
4 analytic + 2 mesh
FEW-SHOT
50
frames, 20 epochs
Three conditions
Zero-shot: áp model sphere trực tiếp.
Few-shot: finetune 50 OOD frames, lr=1e-4.
Scratch: random init với cùng 50-frame budget.
Metric choice
Figure dùng tangential abs-RMSE um.
rel-L2 vẫn lưu trong JSON nhưng phồng khi target norm nhỏ, đặc biệt ellipsoid.

## Slide 35
P8
Phase 8: OOD result table
Bảng native PowerPoint, số từ geometry_ood_phaseE.json
Neural-operator surrogate for VBTS | phase process deck
35
Shape | dist | zero um | few um | scratch um | few delta
sphere_oodR | 0.40 | 17.8 +/- 0.7 | 12.0 +/- 0.4 | 78.2 +/- 0.1 | -32%
rounded_tip | 0.46 | 10.8 +/- 0.7 | 6.1 +/- 0.1 | 50.2 +/- 0.4 | -44%
bolt_hex | 3.36 | 70.5 +/- 0.9 | 51.3 +/- 1.5 | 150.7 +/- 1.9 | -27%
cylinder | 3.86 | 81.2 +/- 0.6 | 60.2 +/- 1.6 | 165.6 +/- 1.3 | -26%
cuboid | 4.28 | 101.7 +/- 2.2 | 81.0 +/- 2.0 | 191.3 +/- 1.0 | -20%
ellipsoid | 4.51 | 102.5 +/- 4.1 | 41.4 +/- 2.7 | 45.9 +/- 0.2 | -60%

## Slide 36
P8
Phase 8: Figure and limitations
Geometry-OOD là điểm yếu được đo và giảm nhẹ, không phải đã giải xong tổng quát hình học
Neural-operator surrogate for VBTS | phase process deck
36
Findings
Zero-shot degrade tăng theo geometry distance.
Few-shot thắng scratch cùng budget.
Finetune tạo specialist, có forgetting trên sphere.
Scope
Không claim distant curved geometry.
Rounded-tip là curved-bottom mesh PoC gần sphere.
Next: multi-geometry foundation/adapters.

## Slide 37
wrap
Tổng kết
Các phase tạo thành một câu chuyện thống nhất: physics-grounded, differentiable, honest about scope
Neural-operator surrogate for VBTS | phase process deck
37
Layer | Đóng góp | Bằng chứng
Ground truth | IPC/UIPC corrected-BC realistic thin gel | 2520 frames, robust adaptive-K
Surrogate | LR-FNO field-to-field | rel-L2 0.0606, 29,182x vs IPC solve
Downstream | control + sensor + env | 72x fewer target queries, image inverse, reward gap 99.8%
Audit | BC root-cause and reground | uniform energy old 99.8% -> corrected 20-24% smoke
Generalization | geometry-OOD quantified | 6 shapes, few-shot recovery 20-60%
Hướng tiếp theo
Multi-geometry foundation model, adapter/few-shot không quên, và sim-to-real calibration trên cảm biến marker-gel thật.